## Slide 1
SequencerGUI()
(creates the GUI)
LatticeSequencerInitialize()
(defines seqdata and adwin communication)
GUI Functions (Callbacks)
initialize_channels()
(defines properties for all adwin channels [names, default settings, calibrations, etc…])
‘Run’ -> cycle_sequence(sequencefunc,waittime,targettime,startcycle,endcycle)
(runs the cycle indicated by sequencefunc)
‘Stop’ -> stop_process()
(attempts to stop cycle after current cycle completes)
‘Abort’ -> abort_process()
(similar to stop, but can abort
A running process. Calls resetADWIN())
‘Reset’ -> resetADWIN()
(calls cycle_sequence with a ‘reset_sequence’
That resets channels to defaults using Reset_Channels)
‘Plot GUI’ -> PlotGUI(hFigure)
(generates list of channels to plot)
getRunStatus()
(queries AdWin run status)
CleanUpTimers()
(this is what actually stops the AdWin)
‘Plot’ -> PlotSequenceVersion2(sequencefunc,startcycle,plotchannels,plot_times)
(Plots channels for the current sequence as specified in the Plot GUI)
cycle_sequence_callback(obj,event,curcycle,endcycle,fhandle,waittime,targettime,newcycle)
(not sure why this also needs to exist, but runs sequence given by fhandle)

## Slide 2
‘Run’ -> cycle_sequence(sequencefunc,waittime,targettime,startcycle,endcycle)
(runs the cycle indicated by sequencefunc)
cycle_sequence_callback(obj,event,curcycle,endcycle,fhandle,waittime,targettime,newcycle)
(not sure why this also needs to exist, but runs sequence given by fhandle)
start_new_sequence()
(A sequence is defined by values in seqdata. Reinitializes seqdata.)
fhandle(0)
(Calls the sequence (typically Load_magTrap_sequence) starting at t=0.
This fills seqdata with a table of times/voltages/channels to send to the Adwin.)
calc_sequence()
(Processes the array into a form Adwin can handle, and also handles DDS/Visa devices. Mercurial server commit also.)
load_sequence()
(Actually load the sequence into the Adwin using libraries for Matlab)

## Slide 3
run_sequence({@cycle_sequence_callback,curcycle,endcycle,fhandle,waittime,targettime,0})
(Starts the actual Adwin process, also saves sequence data in certain hardcoded locations. A timer loops back to cycle_sequence_callback after a wait-time has passed.)
AddToSeqHistory(seqdata,timestamp)
(Tries to store a history of recent sequence data)
FlagsGUI(flags, strings)
(Displays a GUI showing which ‘flags’ have been enabled in seqdata.)
CreateOutputParamFile(outfilename,funcstr)
(Saves output parameters – this always hangs for a long time)